## Slide 1
Types
Dot-matrix printers
Inkjet printing
Laser printing

## Slide 2
Printer does not have power indicator
Cables not connected properly
Printer error (orange or blinking light)
No paper or paper jam(Machine)
Inkjet printer ink related issues(Replace)
Printer self tests (Print)
Printer drivers
Parallel (LPT) printers (BIOS)- llel portEnabled

## Slide 3: Setup printer and install software
Every printer should come with the software used to install a printer in Windows or your operating system.
Connect the printer to the computer either using a USB cable, parallel port cable, or SCSI cable and then connect the power plug to a power outlet.
After everything has been plugged in turn the computer on.
Insert the CD that was included with the printer. If the CD does not automatically start the install program open My Computer, double-click on the CD drive, and then the Setup or Install file. If you've downloaded the drivers, run the downloaded setup file.
Follow the installation wizard and your printer and its associated software should be installed successfully. After installed make sure to test the printer.

## Slide 4: Installing a printer only using the drivers
Connect the printer to the computer and a power outlet and make sure it's on.
Click Start, Settings, and Control Panel.
In the control panel double-click the Printers or Printers and Fax icon.
In the Printers window, click the Add a printer icon.
After completing the above steps, the Windows Printer Wizard will appear. Click Next to start the wizard.
Windows will prompt you if you're installing a Local or Network printer. If the printer is connected to your computer choose Local printer attached to this computer and click Next.
When prompted for the location of the drivers for the printer. Browse the computer to the directory of your drivers or point it to the CD that was included with your printer.

## Slide 5: Testing the printer
Microsoft Windows users
Click Start, Settings, and open Control Panel.
Double-click the Printers or Printers and Fax icon.
Right-click on the Printer you wish to test and click Properties. If you do not see your printer, your printer is not installed.
In the Printers Properties window, click the Print Test Page button.
If the printer is able to print a test page, you're printer is installed and setup properly. However, if you're unable to print in other programs it's possible that the program you're attempting to print from has issues.

## Slide 6: 10 Big Problems
Printing is too slow.
Ink and/or toner costs too much.
Windows is sending print jobs to the wrong printer.